## Slide 1: NTC Overview NTC 0x0A7.0
Description:
This diagnostic is in place to set fault when Handwheel Angle exceeds specific calibratable value (named EotLrngHwAgOverTrvlEntr) and gets back to another calibratable value (named EotLrngHwAgOverTrvlExit) for calibratable number of times (EotLrngHwAgOverTrvlCnt).
Diagnostic Overview:
The diagnostic compares the Handwheel Angle with the Clockwise and Counterclockwise calibratable values. When exceeding Enter value is detected and switch boolean variable is set to FALSE, the counter is incremented by 1. The counter can be incremented again only when the value of Handwheel Angle becomes lesser than the calibratable value. When counter exceeds calibratable count value, the fault is set.
Typical Fault Response:
- Response for this diagnostic is F3
Probable Sources (Most to Least Probable):
    Wrong C-factor cal set
    Connection to probe housing assembly (no connection)
    Sensor fault
    Probe housing assembly interface circuit failure
    Software Rack Limiter failure
Rev: 1.0
Modified: nn-Jan-13
Initialization | 
Periodic | X
Event | 

## Slide 2: Algorithm Changes / Lessons Learned / Revision Log
Date | Revision | Initials
13Jun2016 | Initial Release | SS
Description of Unusual Event setting NTC | Root Cause / Explanation
Date | FDD & Rev | Modifications to Diagnostic Function
13Jun2016 | SF011A 2.1.0 | Initial version
21Nov2016 | SF011A 3.0.0 | New logic of triggering added