## Slide 1: NTC Overview NTC 0x0A5.(0-5) Wheel Imbalance Rejection
Description:
This diagnostic logs a when computed wheel imbalance rejection command has any of the following features
  Exceeds maximum threshold
  DC trend in cancellation command
  Frequency of cancellation is incorrect
  Wheel Speed inputs are incorrect
  Persistance of cancellation command
Diagnostic Overview:
The system function is designed to produce an cancellation command at appropriate frequency, amplitude and phase. If any of the thresholds with respect to amplitude, frequency or phase are exceeded, a diagnostic flag is set
The diagnostic flag shuts down the wheel imbalance cancellation output wither immediately or through controlled ramping depending upon the type of fault
The diagnostic shall also attempt to recover from the fault. Throughout the entire recovery, the final cancellation output shall be zero.
This fault is a recovarable fault and shall reset all the internal variables to start producing the cancellation output from scratch.
Typical Fault Response:
Response for this diagnostic is F3.
This fault is recoverable once the values fall within an ignition cycle.
Probable Sources (Most to Least Probable):
Improper wheel speeds information from serial communication
Maximum magnitude due to very high wheel imbalance
DC Trend in generated cancellation command
Rev: 1.0
Modified: 22MY13
Initialization | 
Periodic | X
Event | 
Bit | Cause
0 | Maximum Magnitude Fault
2 | DC Trend Fault
3 | Frequency Diagnostic Fault
4 | Wheel Speed Correlation Fault
5 | Maximum Persistance Fault

## Slide 2: Algorithm Changes / Lessons Learned / Revision Log
Date | Revision | Initials
08FE16 | Initial Release | JK
10Au16 | Update the bits table with 3 bits used in the NTC | PP
Description of Unusual Event setting NTC | Root Cause / Explanation
Date | FDD & Rev | Modifications to Diagnostic Function