## Slide 1: <PwrpkCmpblty> Overview NTC 0x1F1
FDD: <SF054A>
Description:
The NTC will be SET when the Powerpack is not compatible with the Gear.
This means when either the Gear ID’s are Invalid or they don’t correlate to each other or
don’t correlate with the Gear ID calibration value.
Diagnostic Overview:
The diagnostics will start only after 500msec. Once 500 msec is elapsed, the detection
shall be done and the respective bits of NTC shall be set.
Following is the NTC bit definition
PwrpkCmpblty.NtcStInfo.Bit0Descr = 'Gear ID input #1 timed out or was otherwise invalid';
PwrpkCmpblty.NtcStInfo.Bit1Descr = 'Gear ID input #2 timed out or was otherwise invalid';
PwrpkCmpblty.NtcStInfo.Bit2Descr = 'Gear ID inputs do not correlate to each other';
PwrpkCmpblty.NtcStInfo.Bit3Descr = 'Gear ID inputs do not
Typical Fault Response:
  F3 Notify driver
Probable Sources (Most to Least Probable): Gear ID in PHA does not match Gear ID on CCA
Gear ID’s do not match each other
Gear ID’s are invalid from PHA
Gear ID’s are not provided in less than 500ms
Rev: 1.0
Modified: nn-Jan-13
Initialization | 
Periodic | X
Event | 

## Slide 2: Revision Log
Rev | Revision
6 April 2016 | Initial Release